## Slide 1
SEB INTERNATIONAL SERVICE January 2015
ALL-CLAD ARNO CALOR KRUPS LAGOSTINA
MOULINEX ROWENTA SEB SUPOR TEFAL

## Slide 2
International
Repair
Information
System

## Slide 3: Exchanging Repair Information
.…is facing several difficult problems.
  Different countries,
  Different languages,
  Different types of organization,
  Some different codes,
  …
So, there is a clear need to use an unified, simple codification system.
This code already exist: IRIS CODE.

## Slide 4
IRIS Repair Coding
What is it?

## Slide 5
IRIS Coding basis
The IRIS Code is divided in 4 chapters :
Symptom
Section
Defect
Repair
Technician
Consumer

## Slide 6: Methodology to determine an IRIS code
Consumer :
The consumer describes the defect :
What ?
Example : « My steam generator cuts off the electrical circuit during the ironing »

## Slide 7: Methodology to determine an IRIS code
Consumer : The description of the problem detected by the consumer is based on simple questions which he can answer.
The description depends of the 5 senses :
TO SEE
TO TOUCH
TO SMELL
TO TASTE
TO HEAR

## Slide 8: Methodology to determine an IRIS code
Technician :
The technician must :
Make an analysis, Make a diagnostic
and Bring a solution.
Example : « The boiler is faulty further to an electrical default and I change the part »

## Slide 9: Methodology to determine an IRIS code
To transcribe these actions in an IRIS code.
WHAT ?  Symptom Code
MAKE AN ANALYSIS  Section Code
MAKE A DIAGNOSTIC  Defect Code
BRING A SOLUTION  Repair Code

## Slide 10: IRIS Code implementation  result
Symptom
11H
Section
G77
Defect
S
Repair
A
Internal switch / fuse in set triggers
Boiler
Leaking (electrical)
Replacement (component / module)
Solution
Analysis and Diagnostic
> 5 mA
What
Technician :

## Slide 11: Code
YOUR GO

## Slide 12
Consumer
Technician
Symptom
11F
Section
G40
Defect
N
Repair
A
Solution
Analysis and Diagnostic
My fryer does not work anymore
Replace
1

## Slide 13
Consumer
Technician
Symptom
11F
Section
G18
Defect
N
Repair
A
Solution
Analysis and Diagnostic
Replace
My steamer does not work anymore
--- Ω
2

## Slide 14
Consumer
Technician
Symptom
11H
Section
G13
Defect
N
Repair
A
Solution
Analysis and Diagnostic
My steam generator trips the circuit breaker my electrical installation
Replace
3

## Slide 15
Consumer
Technician
Symptom
M32
Section
G40
Defect
P2
Repair
A
Solution
Analysis and Diagnostic
The soleplate of my steam iron flowing water
Replace
The temperature of the soleplate is too low
4

## Slide 16
Consumer
Technician
Symptom
11F
Section
G30
Defect
D
Repair
A
Solution
Analysis and Diagnostic
Replace
My steam iron does not work anymore
Seal is cut
Other
spare parts
5

## Slide 17
Consumer
Technician
Symptom
11F
Section
G40
Defect
Q
Repair
A
Solution
Analysis and Diagnostic
Replace
My steam iron does not work anymore
6

## Slide 18
Consumer
Technician
Symptom
17S
Section
G40
Defect
C
Repair
A
Solution
Analysis and Diagnostic
My steam iron is not heating enough
Replace
The temperature of the soleplate is too low
7

## Slide 19
Consumer
Technician
Symptom
132
Section
G40
Defect
N
Repair
A
Solution
Analysis and Diagnostic
The indicator "Lack of water" of my steam generator lights all the time
Replace
----Ω
8

## Slide 20
Consumer
Technician
Symptom
11F
Section
G22
Defect
N
Repair
A
Solution
Analysis and Diagnostic
My vacuum cleaner
doesn’t work
Replace
9

## Slide 21
Consumer
Technician
Symptom
121
Section
G68
Defect
N
Repair
A
Solution
Analysis and Diagnostic
My vacuum cleaner will no longer charge and a light blinks steadily
Replace
> 40V dc
10

## Slide 22
Consumer
Technician
Symptom
17G
Section
G73
Defect
M1
Repair
A
Solution
Analysis and Diagnostic
Replace
The cord of my vacuum cleaner no longer fit into its housing
11

## Slide 23
Consumer
Technician
Symptom
N13
Section
G22
Defect
N
Repair
A
Solution
Analysis and Diagnostic
Replace
My espresso no longer grinds coffee beans
13

## Slide 24
Consumer
Technician
Symptom
11F
Section
G61
Defect
4
Repair
U
Solution
Analysis and Diagnostic
My kettle never stops
Info about the functioning of the kettle to the consumer
14

## Slide 25
Consumer
Technician
Symptom
11F
Section
G33
Defect
K
Repair
A
Solution
Analysis and Diagnostic
Replace
My expresso maker does not work anymore
16

## Slide 26
Consumer
Technician
Symptom
11F
Section
G02
Defect
D
Repair
A
Solution
Analysis and Diagnostic
Replace
My espresso does not start
18

## Slide 27
Consumer
Technician
Symptom
J14
Section
G85
Defect
A
Repair
A
Solution
Analysis and Diagnostic
Replace
My mixer blade is no longer rotating
20

## Slide 28
Consumer
Technician
Symptom
164
Section
G81
Defect
H1
Repair
A
Solution
Analysis and Diagnostic
The cover of my food processor is broken
Replace
21

## Slide 29
Consumer
Technician
Symptom
J52
Section
G30
Defect
K
Repair
A
Solution
Replace
The bowl of my blender leaks
22
Analysis and Diagnostic

## Slide 30
DEMONSTRATION
http://www.iriscode.org/